## Slide 1: Arduino Course Session Two
PWM signal & DC motor control (& servo motor if possible)

## Slide 2: Session 1 Wrap-Up
Installed and used Arduino IDE
Explored Arduino Layout
Digital Output functions (commands):
  pinMode(<pin>, <usage>) e.g.(pinMode(9, OUTPUT);)
  digitalWrite(<pin>, <HIGH/LOW>)
Delay
Average Voltage for high frequency signal

## Slide 3: Session 2 Objective
Why voltage is averaged
PWM, what it is, how to use it, types of it
Serial Monitor
Variables
Transistors
Motors
H-Bridge
Bidirectional motors
Motor control IC

## Slide 4: Averaging of High Frequency Signal (when using small amount of delay)
digitalWrite(pin, HIGH);
delay(3);
digitalWrite(pin, LOW);
delay(1);
T=4ms

## Slide 5: Averaging of High Frequency Signal (when using small amount of delay)

## Slide 6: Pulse Width Modulation (our version)
Pulse Width
digitalWrite(pin, HIGH);
delay(pulse width);
digitalWrite(pin, LOW);
delay(period – pulse width)
Pulse Width Modulation:
Pulse

## Slide 7: Problem of software PWM

## Slide 8: Hardware PWM

## Slide 9: Hardware PWM
Dedicated PWM device built-in Arduino
Function to control it:
  analogWrite(pin, value);
  This value is base on pwm device resolution, in Arduino Uno it is 8-bit so 0 till 255

## Slide 10: Basic Serial Communication with Laptop
Setup the communication device to open a serial port with the PC
Use function <Serial.Println(<string/int>) to send the string or integer to the serial monitor
Note: Serial Communication is a broad way of communication containing many protocols, the protocol we are currently using for code upload and printing over serial is called UART

## Slide 11: Bidirectional Motor Control – H bridge